SECTION 097710 – FABRIC-WRAPPED PANELS

GENERAL

SUMMARY

This Section includes the following:

Fabric –wrapped panels.

SUBMITTALS

Product Data:  For each type of panel edge, backing material, and mounting indicated.

Product Data:  For each type of product indicated.

Shop Drawings:  Submit shop drawings showing how panels are to be laid out on walls and ceilings.  Width of panels and location of vertical seams are critical.

QUALITY ASSURANCE

Single-Source Responsibility:  Provide panel units and installation components by a single manufacturer.

Fire Performance Characteristics:  Identify acoustical wall components with appropriate markings of applicable testing and inspecting organization.

Surface Burning Characteristics:  As follows for Class A, tested per ASTM E 84.

Flame Spread:  0 - 25.

Smoke Developed:  0 - 450.

Coordination of Work:  Coordinate panel work with installers of related work including, but not limited to building insulation, gypsum board, light fixtures, mechanical systems, electrical systems, and sprinklers.

DELIVERY, STORAGE, AND HANDLING

Deliver panels to project site in original, unopened packages and store them in a fully enclosed space where they will be protected against damage from moisture, direct sunlight, surface contamination, and other causes.

Handle acoustical metal panels carefully to avoid scratching or damaging units in any way.

PRODUCTS

MANUFACTURERS

Fabric-Wrapped Panels:

Wallmate, Fabric Wallmount System by Acoustical Surfaces, Inc. (Basis of Design)

123 Columbia Court North, Suite 201, Chaska, MN 55318.

952-448-5300, Fax: 952-448-2613.

Toll Free: 1-800-448-3134.

Or equal.

FABRIC-WRAPPED PANELS

Product: Wallmate by Acoustical Surfaces, Inc or equal.

Description: Site fabricated, fabric wrapped panels stretched and locked into various edge profiles.

Fabric: Standard Guilford FR 701 Fabric Facings or any decorative fabric of choice.

Color: As selected by Architect.

Edge Mount (Options):

Bevel: 9/16 or 1-1/16 inch.

Radius: 9/16 or 1-1/16 inch.

Square: 9/16 or 1-1/16 inch.

Acoustical Backing Material (Optional): Echo Eliminator by Acoustical Surfaces, Inc.

NRC Values for following thickness:

1 inch thick (3lb/cf): 0.80.

2 inch thick (3lb/cf): 1.15.

1 inch thick (6lb/cf): 0.85.

Panel Fire Test per ASTM E84: Class A.

Flame Spread: 5.

Smoke Developed: 35.

Panel Sizes: Custom sizes as indicted on Drawings.

Panel Thicknesses: 1 or 2 inches.

Panel System (Fabric, acoustical backing material, edge moldings combined) Fire Test per ASTM E84: Class A.

Flame Spread: 15.

Smoke Developed: 145.

Feature: Economical, Multi-Purpose, High Performance, Durable, Easy to install.

Applications: Offices, Residences, Meeting Rooms, Apartments, Condominiums, Board Rooms, Auditoriums.

EXECUTION

PREPARATION

Measure each area and establish layout of acoustical units to balance border widths at opposite edges of each area.  Coordinate metal panel layout with mechanical and electrical fixtures.

INSTALLATION

Install panels per the manufacturer’s written instructions.

CLEANING

Clean exposed panel surfaces.  Comply with manufacturer's written instructions for cleaning, and minor finish damage repairs.  Remove and replace panel components that cannot be successfully cleaned and repaired to permanently eliminate evidence of damage, including deformed panels.

END OF SECTION 097710