SECTION 097711 – FABRIC-WRAPPED ACOUSTICAL BAFFLES

GENERAL

SUMMARY

This Section includes the following:

Fabric wrapped acoustical baffles.

SUBMITTALS

Product Data:  For each type of baffle edge, core material, and mounting indicated.

Product Data:  For each type of product indicated.

Shop Drawings:  Submit shop drawings showing how baffles are to be hung on ceilings. Width of baffle and location of vertical seams are critical.

QUALITY ASSURANCE

Single-Source Responsibility:  Provide baffle units and installation components by a single manufacturer.

Fire Performance Characteristics:  Identify acoustical wall components with appropriate markings of applicable testing and inspecting organization.

Surface Burning Characteristics:  As follows for Class A, tested per ASTM E 84.

Flame Spread:  0 - 25.

Smoke Developed:  0 - 450.

Coordination of Work:  Coordinate baffle work with installers of related work including, but not limited to building insulation, gypsum board, light fixtures, mechanical systems, electrical systems, and sprinklers.

DELIVERY, STORAGE, AND HANDLING

Deliver baffles to project site in original, unopened packages and store them in a fully enclosed space where they will be protected against damage from moisture, direct sunlight, surface contamination, and other causes.

Handle acoustical baffles carefully to avoid scratching or damaging units in any way.

PRODUCTS

MANUFACTURERS

Fabric-Wrapped Acoustical Baffles:

Fabrisorb by Acoustical Surfaces, Inc. (Basis of Design)

123 Columbia Court North, Suite 201, Chaska, MN 55318.

952-448-5300, Fax: 952-448-2613.

Toll Free: 1-800-448-3134.

Or equal.

FABRIC-WRAPPED ACOUSTICAL BAFFLES

Product: Fabrisorb by Acoustical Surfaces, Inc or equal.

Description: Decorative, fabric wrapped acoustical baffles.

Baffle Sizes: Custom sizes as indicted on Drawings.

Type 1:

Construction: One piece lightweight 7PCF fiber core with square or radius edges and covered on all sides with fabric.

Mounting: Eyehooks

Thickness: 1, 1-1/2, and 2 inches.

Type 2:

Construction: Two pieces of 7PCF glass fiber with square or radius edges with perforated vinyl or fabric.

Mounting: D-rings

Thickness: 1, 1-1/2, and 2 inches.

Fabric: Standard Guilford FR 701 Fabric Facings or any decorative fabric of choice.

Color: As selected by Architect.

Acoustical Performance (Sabins per 48″ × 24″ Unit, fabric covered glass fiber core):

Type 1: 1 inch thick, 10.45 Sabins.

Type 2: 2 inches thick, 14.02 Sabins.

Baffle Fire Test per ASTM E84: Class A.

Flame Spread: 15.

Smoke Developed: 40.

EXECUTION

PREPARATION

Measure each area and establish layout of acoustical units to balance border widths at opposite edges of each area.  Coordinate baffle layout with mechanical and electrical fixtures.

INSTALLATION

Install baffles per the manufacturer’s written instructions.

CLEANING

Clean exposed baffle surfaces.  Comply with manufacturer's written instructions for cleaning, and minor finish damage repairs.  Remove and replace baffles that cannot be successfully cleaned and repaired to permanently eliminate evidence of damage, including deformed baffles.

END OF SECTION 097711